## Slide 1: Computer Networks
Lecture 3: Data Link - part II
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2: Data Link Layer
Function:
  Send blocks of data (frames) between physical devices
  Regulate access to the physical media
Key challenge:
  How to delineate frames?
  How to detect errors?
  How to perform media access control (MAC)?
  How to recover from and avoid collisions?
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Outline
Framing
Error Checking and Reliability
Media Access Control
  802.3 Ethernet
  802.11 Wifi

## Slide 4: Error control
Error Control Strategies
  Error Correcting codes (Forward Error Correction (FEC))
  Error detection and retransmission Automatic Repeat Request (ARQ)

## Slide 5: Error control
Objectives
  Error detection
    with correction
      Forward error correction
    without correction -> e.g. drop a frame
      Backward error correction
      The erroneous frame needs to be retransmitted
  Error correction
    without error detection
      e.g. in voice transmission

## Slide 6: Should We Error Check in the Data Link?
Recall the End-to-End Argument
Cons:
  Error free transmission cannot be guaranteed
  Not all applications want this functionality
  Error checking adds CPU and packet size overhead
  Error recovery requires buffering
Pros:
  Potentially better performance than app-level error checking
Data link error checking in practice
  Most useful over lossy links
  Wifi, cellular, satellite

## Slide 7: Backward Error Correction

## Slide 8: Backward error correction
Network Layer
Data Link Layer
Physical Layer
Network Layer
Data Link Layer
from_upper(p)
to_lower(p)
to_upper(p)
from_lower(p)
Packets
Frames
Bits
Error detection at the receiver side
The sender retransmits a frame until it received by the other side correctly.

## Slide 9: Model of Frame Transmission

## Slide 10: Elementary Data Link Protocols
Simplex Stop-and-Wait Protocol
Alternate Bit Protocol
Sliding Window Protocol

## Slide 11: Simple Stop-and-Wait Protocol
A sends a message to B
A stops and waits for an answer from B
  Acknowledgement message (ACK)
After receiving the message B sends an ACK back to the sender.
A retransmits the message until it receives an ACK from B
If the ACK arrived, the next message may be sent.

## Slide 12: Simplex Stop-and-Wait Protocol
Sender
Receiver

## Slide 13: Stop-and-Wait Link Utilization

## Slide 14: Stop-and-Wait Diagram
Simple, but inefficient for long distance and high speed applications.
We can use sliding-window technique to improve the efficiency.

## Slide 15: What’s the problem?
Usually
Packet loss
ACK loss

## Slide 16: Alternating Bit Protocol (ABP)
Let
  A be the sender
  B be the receiver
A and B maintain internal one-bit counter
  A value that is 0 or 1
Each message from A to B contains
  a data part and
  a one-bit sequence number
    E.g. a value that is 0 or 1
After receiving A’s message, B sends an ACK back to A
  which also contains a one-bit sequence number
Retransmission until A receives an ACK from B with the same sequence number
  Then A complements its sequence number
    0->1 or
    1->0

## Slide 17: Alternating Bit Protocol (ABP)
Sender
Receiver

## Slide 18: Alternating Bit Protocol (ABP)
A reliable data transport over a noisy channel
Basic flow control
  The sender has to wait for the ACK from the receiver before sending the next message
Automatic Repeat reQest (ARQ) protocol
An acknowledgement
  marks that the new message has been delivered.
  allows the sender to tranmit the next frame.

## Slide 19: Alternating Bit Protocol
Two scenarios for ABP. (a) Normal case. (b) Abnormal case. The notation is (seq, ack, packet number). An asterisk indicates where a network layer accepts a packet.

## Slide 20: ABP – Channel utilization
Utilization (η) is the ratio of
  The time needed for the transmission of a frame (Tpacket)
  The time ellapsed until the next frame can be transmitted
    In the fig.: (Tpacket + d + Tack + d)
Now:
  η = Tpacket / (Tpacket + d + Tack + d)
If the propagation delay is large, the ABP is not efficient.
Time

## Slide 21: How to improve the efficency?
The sender transmit frames continously one after another
  More frames are sent out, but not acknowledged.
  Pipeline technique
Introduce sequence numbers
Time

## Slide 22: Sliding Window Protocols
Similar to ABP
but allow multiple frames to transmit
  Receiver has a buffer of W frames
  Sender can send up to W frames without receiving ACK
Bidirectional
Each outgoing frame contains a seq. number from 0 to 2n-1.
  So it fits in an n-bit field
  ABP uses n=1
Each ACK carries the sequence number of the next expected frame by the receiver

## Slide 23: Sliding Window Protocols
At the sender
  Sending window
    a set of sequence numbers corresponding to frames being under transmission (finite range of numbers)
At the receiver
  Receiving window
    Sequence numbers for frames it is permitted to accept (finite range of numbers)
The sender’s and receiver’s windows need
  not have tha same lower and upper bounds and
  even have the same size.
The window size can be
  fixed or
  grow or shrink over the course of time as frames are sent and received

## Slide 24: Sliding-Window Diagram
Need to buffer them in case of retransmission
Notes: Assume 3-bit sequence number is used. Frames are numbered sequentially from 0 through 7.
In Fig.(a), each time a frame is sent, the shaded window shrinks; each time an ACK is received, the shaded window grows.

## Slide 25: Example Sliding-Window
RR3 means the receiver has received all frames up to frame 2 and is ready to receive frame 3.
Have been delivered to upper layer
More spaces for future frames
Notes: It is not necessary to acknowledge every frame.

## Slide 26: Sliding Window Protocols
A sliding window of size 1, with a 3-bit sequence number.
(a) Initially.
(b) After the first frame has been sent.
(c) After the first frame has been received.
(d) After the first acknowledgement has been received.

## Slide 27: Go-Back-N
A sliding window protocol where
  the receiver’s window size is fixed to 1,
  while the sender has window size > 0.
After receiving a damaged frame
  Receiver discards all subsequent frames
  Sender retransmits the damaged frame and all its successors after the times out

## Slide 28: Go-Back-N

## Slide 29: Selective Repeat
Receiver’s window size is n ( n >1 )
  At most n frames can be buffered
Receiver stores all the correct frames following the bad one
The sender retransmits only the bad frame not all its successors

## Slide 30: Selective Repeat

## Slide 31: Communication channels and piggybacking
Simplex
  Communication in one direction only
Half-duplex
  Communication in both directions, but only one direction at a time, not simultaneously.
Full-duplex
  Communication in both directions simultaneously
The previous protocols assumed
  a simplex channel to the upper (network) layer and
  a (half-)duplex channel to the physical layer
If we use duplex channel to the upper layers
  Transmitting data packet and acknowledgements in both directions separately
  Or using piggybacking
    The header of a data packet sent in the opposite direction carries the acknowledgement back to the other side
    widely applied in practice

## Slide 32: Ethernet frame

## Slide 33: Outline
Framing
Error Checking and Reliability
Media Access Control
  802.3 Ethernet
  802.11 Wifi

## Slide 34: What is Media Access?
Ethernet and Wifi are both multi-access technologies
  Broadcast medium, shared by many hosts
  Simultaneous transmissions cause collisions
    This destroys the data
Media Access Control (MAC) protocols are required
  Rules on how to share the medium
  Strategies for detecting, avoiding, and recovering from collisions

## Slide 35: Strategies for Media Access
Channel partitioning
  Divide the resource into small pieces
  Allocate each piece to one host
  Example: Time Division Multi-Access (TDMA) cellular
  Example: Frequency Division Multi-Access (FDMA) cellular
Taking turns
  Tightly coordinate shared access to avoid collisions
  Example: Token ring networks

## Slide 36: Channel Partitioning
Frequency Division Multiplexing
  E.g. a telephone trunk
Time Division Multiplexing
Are they good solutions?
  if data rates are fixed
  if the link utilization is good

## Slide 37: What’s the problem?
The number of senders is large
continuously varying
bursty traffic

## Slide 38: Bursty traffic
If there’s huge difference between the peak rate and the mean (or average) rate
In computer networks it is not rare
  peak rate/mean rate = 1000/1

## Slide 39: Bursty traffic with Static Channel Allocation
The capacity of the channels must be
  Either quite large to handle peak rates
    Waste of resources
    The mean rate is much less than the peak one
  Or based on the mean rate
    We need buffers/queues to store packets coming faster than the mean rate
    Queuing delays
BUFFERS
Incoming packets

## Slide 40: What’s about delays?
If there’s no multiplexing
  A source has data rate of p bps
  The capacity of the link is C bps
  The delay is T
Bursty traffic with static channel allocation
  Dividing the channel into N static subchannels
    With sending rate p/N bps and capacity C/N
  The delay is N T
Static channel allocation increases the packet delays
Because of the idle subchannels

## Slide 41: CDMA – Code Division Multiple Access

## Slide 42: CDMA Analogy
10 people in a room.
  5 speak English, 2 speak Spanish, 2 speak Chinese, and 1 speaks Russian.
Everyone is talking at relatively the same time over the same medium – the air.
Who can listen to whom and why?
Who can’t you understand?
Who can’t speak to anyone else?

## Slide 43: CDMA – Code Division Multiple Access
Used by 3G and 4G cellular networks
Each station can broadcast at any time in the full frequency spectrum
The signals may interfere
  Resulting in a linear combination of individual signals
Algorithm
  We assign a vector of length m to each station: v
    Pairwise orthogonal vectors!!!
  Each bit is encoded by the chip vector of the sender or it’s complement: v or -v
  If it sends bit 1, it transmits v
  If it sends bit 0, it transmits -v
Result is a sequence of vectors of length m

## Slide 44: CDMA – Code Division Multiple Access
Interference
  A sends a,-a,a,a
  B sends b,b,-b,-b
  After interference we receive: a+b,-a+b,a-b,a-b ???
How to decode?

## Slide 45: CDMA – Code Division Multiple Access
Interference
  A sends a,-a,a,a
  B sends b,b,-b,-b
  After interference we receive: a+b,-a+b,a-b,a-b ???
Decoding the message of A
  Take the dot product by the sender’s chip code
    (a+b)a > 0 => 1
    (-a+b)a < 0 => 0
    (a-b)a >0 => 1
    (a-b)a > 0 => 1
  If the dot product is
  <0: bit 0 was sent by A
  >0: bit 1 was sent by A
  =0: nothing was sent by A
  the channel is not used by A