## Slide 1: Computer Networks
Lecture 6a: Interconnecting LANs
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2: Just Above the Data Link Layer
Bridging
  How do we connect LANs?
Function:
  Route packets between LANs
Key challenges:
  Plug-and-play, self configuration
  How to resolve loops
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Recap
Pros: Simplicity
  Hardware is stupid and cheap
Cons: No scalability
  More hosts = more collisions = pandemonium
Originally, Ethernet was a broadcast technology
Tee Connector
Terminator
Hub
Repeater

## Slide 4: Bridging the LANs
Bridging limits the size of collision domains
  Vastly improves scalability
  Question: could the whole Internet be one bridging domain?
Tradeoff: bridges are more complex than hubs
  Physical layer device vs. data link layer device
  Need memory buffers, packet processing hardware, routing tables
Hub
Hub

## Slide 5: Bridges
Original form of Ethernet switch
Connect multiple IEEE 802 LANs at layer 2
Goals
  Reduce the collision domain
  Complete transparency
    “Plug-and-play,” self-configuring
    No hardware of software changes on hosts/hubs
    Should not impact existing LAN operations
Hub
Forwarding of frames
Learning of (MAC) Addresses
Spanning Tree Algorithm (to handle loops)

## Slide 6: Frame Forwarding Tables
00:00:00:00:00:DD | 1 | 3 minutes
Each bridge maintains a forwarding table
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 1 minute
00:00:00:00:00:BB | 2 | 7 minutes
00:00:00:00:00:CC | 3 | 2 seconds

## Slide 7: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error Prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port
Hub
00:00:00:00:00:AA
00:00:00:00:00:BB
Port 1
Port 2
00:00:00:00:00:BB | 2 | 0 minutes
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 0 minutes
Delete old entries after a timeout

## Slide 8: The Danger of Loops
<Src=AA, Dest=DD>
This continues to infinity
  How do we stop this?
Remove loops from the topology
  Without physically unplugging cables
802.1 (LAN architecture) uses an algorithm to build and maintain a spanning tree for routing
AA
Port 1
Hub
Port 1
Hub
Port 2
Port 2
AA | 1
AA | 1
BB
CC
DD
AA | 2
AA | 2
AA | 1
AA | 1

## Slide 9: Spanning Tree Definition
A subset of edges in a graph that:
  Span all nodes
  Do not create any cycles
This structure is a tree
1
4
2
5
6
3
7
1
4
2
5
6
3
7
5
1
4
2
6
3
7

## Slide 10: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 11: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BPDUs:
Based on received BPDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to root)
Root ID
Path Cost to Root
Bridge ID

## Slide 12: Spanning Tree Construction
0: 0/0
12: 12/0
3: 3/0
27: 27/0
41: 41/0
9: 9/0
68: 68/0
27: 0/1
12: 0/1
41: 3/1
68: 9/1
41: 0/2
3: 0/2
68: 3/2
9: 3/2
68: 0/3
9: 0/3

## Slide 13: Bridges vs. Switches
Bridges make it possible to increase LAN capacity
  Reduces the amount of broadcast packets
  No loops
Switch is a special case of a bridge
  Each port is connected to a single host
    Either a client machine
    Or another switch
  Links are full duplex
  Simplified hardware: no need for CSMA/CD!
  Can have different speeds on each port

## Slide 14: Switching the Internet
Capabilities of switches:
  Network-wide routing based on MAC addresses
  Learn routes to new hosts automatically
  Resolve loops
Could the whole Internet be one switching domain?
NO
Notes: Flooding packets until routes figured out
No load balancing
Addressing!

## Slide 15: Limitations of MAC Routing
Inefficient
  Flooding packets to locate unknown hosts
Poor Performance
  Spanning tree does not balance load
  Hot spots
Extremely Poor Scalability
  Every switch needs every MAC address on the Internet in its routing table!
  IP addresses these problems (next …)

## Slide 16: Computer Networks
Lecture 6b: Network Layer
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 17: Network Layer
Function:
  Route packets end-to-end on a network, through multiple hops
Key challenge:
  How to represent addresses
  How to route packets
    Scalability
    Convergence
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 18: Routers, Revisited
How to connect multiple LANs?
LANs may be incompatible
  Ethernet, Wifi, etc…
Connected networks form an internetwork
  The Internet is the best known example
Routers

## Slide 19: Internetworking Issues
Naming / Addressing
  How do you designate hosts?
Routing
  Must be scalable (i.e. a switched Internet won’t work)
Service Model
  What gets sent?
  How fast will it go?
  What happens if there are failures?
  Must deal with heterogeneity
    Remember, every network is different
Internet Service Model
Best-effort (i.e. things may break)
Store-and-forward datagram network
Lowest common denominator

## Slide 20: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 21: Possible Addressing Schemes
Flat
  e.g. each host is identified by a 48-bit MAC address
  Router needs an entry for every host in the world
    Too big
    Too hard to maintain (hosts come and go all the time)
    Too slow (more later)
Hierarchy
  Addresses broken down into segments
  Each segment has a different level of specificity
Notes: If time, show correlation between lookup speed and maximum line rate

## Slide 22: Example: Telephone Numbers
1-617-373-1234
West Village H
Room 256
Very General
Very Specific
West Village G
Room 1234
3278
Updates are Local

## Slide 23: Binary Hierarchy Example
1**
10*
11*
100
101
110
111
0**
00*
01*
000
001
010
011
Datagram, Destination = 101

## Slide 24: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g. 192.168.21.76
  Each number is a byte
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31

## Slide 25: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers

## Slide 26: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: NEU
129.10.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24

## Slide 27: How Do You Get IPs?
IP address ranges controlled by IANA
  Internet Assigned Number Authority
  Roots go back to 1972, ARPANET, UCLA
  Today, part of ICANN
IANA grants IPs to regional authorities
  ARIN (American Registry of Internet Numbers) may grant you a range of IPs
  You may then advertise routes to your new IP range
  There are now secondary markets, auctions, …

## Slide 28: Two Level Hierarchy
…
…
Host
Network
Subtree size determined by network class
Pfx

## Slide 29: Class Sizes
Class | Prefix Bits | Network Bits | Number of Classes | Hosts per Class
A | 1 | 7 | 27 – 2 = 126 (0 and 127 are reserved) | 224 – 2 = 16,777,214 (All 0 and all 1 are reserved)
B | 2 | 14 | 214 = 16,398 | 216 – 2 = 65,534 (All 0 and all 1 are reserved)
C | 3 | 21 | 221 = 2,097,512 | 28 – 2 = 254 (All 0 and all 1 are reserved)
 |  |  | Total: 2,114,036 | 
Too many network IDs
Too small to be useful
Way too big

## Slide 30: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:

## Slide 31: Subnet Example
Extract network:
Extract host:
10110101 11011101 01010100 01110010
IP Address:
& 11111111 11111111 11000000 00000000
Subnet Mask:
10110101 11011101 01000000 00000000
Result:
10110101 11011101 01010100 01110010
IP Address:
& ~(11111111 11111111 11000000 00000000)
Subnet Mask:
00000000 00000000 00010100 01110010
Result:

## Slide 32: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks

## Slide 33: Example Routing Table
Address Pattern | Subnet Mask | Destination Router
0.0.0.0 | 0.0.0.0 | Router 4
18.0.0.0 | 255.0.0.0 | Router 2
128.42.0.0 | 255.255.0.0 | Router 3
128.42.128.0 | 255.255.128.0 | Router 5
128.42.222.0 | 2555.255.255.0 | Router 1
Question: 128.42.222.198 matches four rows
  Which router do we forward to?
Longest prefix matching
  Use the row with the longest number of 1’s in the mask
  This is the most specific match

## Slide 34: Subnetting Revisited
Question: does subnetting solve all the problems of class-based routing?
NO
Classes are still too coarse
  Class A can be subnetted, but only 126 available
  Class C is too small
  Class B is nice, but there are only 16,398 available
Routing tables are still too big
  2.1 million entries per router

## Slide 35: Classless Inter Domain Routing
CIDR, pronounced ‘cider’
Key ideas:
  Get rid of IP classes
  Use bitmasks for all levels of routing
  Aggregation to minimize FIB (forwarding information base)
Arbitrary split between network and host
  Specified as a bitmask or prefix length
  Example: Stony Brook
    130.245.0.0 with netmask 255.255.0.0
    130.245.0.0 / 16

## Slide 36: Aggregation with CIDR
Original use: aggregating class C ranges
One organization given contiguous class C ranges
  Example: Microsoft, 207.46.192.* – 207.46.255.*
  Represents 26 = 64 class C ranges
  Specified as CIDR address 207.46.192.0/18
11001111
CF
207
00101110
2E
46
11xxxxxx
C0
192
xxxxxxxx
00
0
Decimal
Hex
Binary
0
8
16
24
31
18 Bits Frozen By Netmask
14 Arbitrary Bits

## Slide 37: Size of CIDR Routing Tables
From www.cidr-report.org
CIDR has kept IP routing table sizes in check
  Currently ~500,000 entries for a complete IP routing table
  Only required by backbone routers

## Slide 38: We had a special day in summer 2014!
512K day – August 12, 2014
Default threshold size for IPv4 route data in older Cisco routers  512K routes
  Some routers failed over to slower memory
    RAM vs. CAM (content addressable memory)
  Some routes dropped
Cisco issues update in May anticipating this issue
  Reallocated some IPv6 space for IPv4 routes
Part of the cause
  Growth in emerging markets
http://cacm.acm.org/news/178293-internet-routing-failures-bring-architecture-changes-back-to-the-table/fulltext

## Slide 39: Takeaways
Hierarchical addressing is critical for scalability
  Not all routers need all information
  Limited number of routers need to know about changes
Non-uniform hierarchy useful for heterogeneous networks
  Class-based addressing is too course
  CIDR improves scalability and granularity
Implementation challenges
  Longest prefix matching is more difficult than schemes with no ambiguity