## Slide 1: Computer Networks
Lecture 2: Physical layer +
Data Link layer
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2
Static Channel Allocation

## Slide 3: Multiplexing
Enabling multiple signals to travel through the same media at the same time
To this end, the channel is split into multiple smaller subchannels
A special device (multiplexer) is needed at the sender, transmitting signals to the proper subchannel

## Slide 4: Space-Division Multiplexing
Simplest way of multiplexing
Wired example: point-to-point wire for each subchannel
Wireless example: Different antennas for the subchannels

## Slide 5: Frequency-Division Multiplexing
Multiple signals are combined and transmitted over the channel
Each signal is transmitted in different frequency ranges
Typically used for analog transmission
Multiple implementations…

## Slide 6: Wavelength-Division Multiplexing
Used for optical cables
IR laser rays at different wavelengths
TR1
TR2
TR3
TR4
W
D
M
W
D
M
TR1
TR2
TR3
TR4
Notes: Több szignált kombinál össze lézersugarakkal különféle infravörös hullámhosszokon az optikai kábelen történő átvitelhez,
míg a fogadó oldalon különféle filterek használ a
hullámhosszok elkülönítésére.
MINDEN EGYES LÉZER önálló szignál halmazt alkalmaz
Jeladó (TR)
Klasszikus változatban 2 hullámhossz volt

## Slide 7: Time-Division Multiplexing
Time is divided into not overlapping intervals
Each time slot is assigned to a sender, exlusively.
Empty slots may happen.
A
B
C
A
B
C
T
D
M
T
D
M
A
B
B
C
A
C

## Slide 8: CDMA – Code Division Multiple Access

## Slide 9: CDMA Analogy
10 people in a room.
  5 speak English, 2 speak Spanish, 2 speak Chinese, and 1 speaks Russian.
Everyone is talking at relatively the same time over the same medium – the air.
Who can listen to whom and why?
Who can’t you understand?
Who can’t speak to anyone else?

## Slide 10: CDMA – Code Division Multiple Access
Used by 3G and 4G cellular networks
Each station can broadcast at any time in the full frequency spectrum
The signals may interfere
  Resulting in a linear combination of individual signals
Algorithm
  We assign a vector of length m to each station: v
    Pairwise orthogonal vectors!!!
  Each bit is encoded by the chip vector of the sender or it’s complement: v or -v
  If it sends bit 1, it transmits v
  If it sends bit 0, it transmits -v
Result is a sequence of vectors of length m

## Slide 11: CDMA – Code Division Multiple Access
Interference
  A sends a,-a,a,a
  B sends b,b,-b,-b
  After interference we receive: a+b,-a+b,a-b,a-b ???
How to decode?

## Slide 12: CDMA – Code Division Multiple Access
Interference
  A sends a,-a,a,a
  B sends b,b,-b,-b
  After interference we receive: a+b,-a+b,a-b,a-b ???
Decoding the message of A
  Take the dot product by the sender’s chip code
    (a+b)a > 0 => 1
    (-a+b)a < 0 => 0
    (a-b)a >0 => 1
    (a-b)a > 0 => 1
  If the dot product is
  <0: bit 0 was sent by A
  >0: bit 1 was sent by A
  =0: nothing was sent by A
  the channel is not used by A

## Slide 13: Data Link Layer
Function:
  Send blocks of data (frames) between physical devices
  Regulate access to the physical media
Key challenge:
  How to delineate frames?
  How to detect errors?
  How to perform media access control (MAC)?
  How to recover from and avoid collisions?
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 14: Outline
Framing
Error Checking and Reliability
Media Access Control
  802.3 Ethernet
  802.11 Wifi

## Slide 15: Framing
Physical layer determines how bits are encoded
Next step, how to encode blocks of data
  Packet switched networks
  Each packet includes routing information
  Data boundaries must be known so headers can be read
Types of framing
  Byte oriented protocols
  Bit oriented protocols
  Clock based protocols

## Slide 16: Byte Oriented: Byte Stuffing
Add FLAG bytes as sentinel to the beginning and end of the data
Problem: what if FLAG appears in the data?
  Add a special DLE (Data Link Escape) character before FLAG
  What if DLE appears in the data? Add DLE before it.
  Similar to escape sequences in C
    printf(“You must \”escape\” quotes in strings”);
    printf(“You must \\escape\\ forward slashes as well”);
Used by Point-to-Point protocol, e.g. modem, DSL, cellular
Data
FLAG
FLAG
FLAG
DLE
DLE
DLE

## Slide 17: Byte Oriented: Byte Counting
Sender: insert length of the data in bytes at the beginning of each frame
Receiver: extract the length and read that many bytes
What happens if there is an error transmitting the count field?
Data
132
132

## Slide 18: Bit Oriented: Bit Stuffing
Add sentinels to the start and end of data (similarly to byte stuffing)
  Both sentinels are the same
  Example: 01111110 in High-level Data Link Protocol (HDLC)
Sender: insert a 0 after each 11111 in data
  Known as “bit stuffing”
Receiver: after seeing 11111 in the data…
  111110  remove the 0 (it was stuffed)
  111111  look at one more bit
    1111110  end of frame
    1111111  error! Discard the frame
Disadvantage: 20% overhead at worst
What happens if error in sentinel transmission?
Data
01111110
01111110
Notes: HDLC used in SoNET phone

## Slide 19: Clock-based Framing: SONET
Synchronous Optical Network
  Transmission over very fast optical links
  STS-n, e.g. STS-1: 51.84 Mbps, STS-768: 36.7 Gbps
STS-1 frames based on fixed sized frames
  9*90 = 810 bytes  after 810 bytes look for start pattern
Physical layer details
  Bits are encoded using NRZ
  Payload is XORed with a special 127-bit pattern to avoid long sequences of 0 and 1
90 Columns
9 Rows
Payload
Overhead
Special start pattern

## Slide 20: Outline
Framing
Error Checking
Media Access Control
  802.3 Ethernet
  802.11 Wifi

## Slide 21: Dealing with Noise
The physical world is inherently noisy
  Interference from electrical cables
  Cross-talk from radio transmissions, microwave ovens
  Solar storms
How to detect bit-errors in transmissions?
How to recover from errors?

## Slide 22: Naïve Error Detection
Idea: send two copies of each frame
  if (memcmp(frame1, frame2) != 0) { OH NOES, AN ERROR! }
Why is this a bad idea?
  Extremely high overhead
  Poor protection against errors
    Twice the data means twice the chance for bit errors

## Slide 23: Parity Bits
Detects 1-bit errors and some 2-bit errors
Not reliable against bursty errors
Idea: add extra bits to keep the number of 1s even
  Example: 7-bit ASCII characters + 1 parity bit
0101001
1
0
1
1
1
1011110
0110100
1101001
0001110
1
10

## Slide 24: Error control
Error Control Strategies
  Error Correcting codes (Forward Error Correction (FEC))
  Error detection and retransmission Automatic Repeat Request (ARQ)

## Slide 25: Error control
Objectives
  Error detection
    with correction
      Forward error correction
    without correction -> e.g. drop a frame
      Backward error correction
      The erroneous frame needs to be retransmitted
  Error correction
    without error detection
      e.g. in voice transmission

## Slide 26: Redundancy
Redundancy is required for error control
Without redundancy
  2m possible data messages can be represented as data on m bits
  They all are legal!!!
  Each error results a new legal data message
How to detect errors???
Legal frames
All the possible
frames

## Slide 27: Error-correcting codes Redundancy
A frame consists of
  m data bits (message)
  r redundant/check bits
  The total length n = m + r
This n-bit unit is referred to as an n-bit codeword!
Legal frames
All the possible frames

## Slide 28: Error

## Slide 29: Hamming distance
1. The Hamming distance d(000, 011) is 2 because
2. The Hamming distance d(10101, 11110) is 3 because
The Hamming distance between two codewords is the number of differences between corresponding bits.

## Slide 30: Hamming distance
If not all the 2n possible codewords are used
  Set of legal codewords =: S
Hamming distance of the complete code
  The smallest Hamming distance of between all the possible pairs in the set of legal codewords (S)

## Slide 31: What is the Hamming distance?
Two examples:

## Slide 32: Error detection
To detect d errors, you need a distance d+1 code.

## Slide 33: Error correction
To correct d errors, you need a distance 2d+1 code.

## Slide 34: Example
S={ 00000000,
00001111,
11110000,
11111111
}

## Slide 35: Parity bit – already discussed
A single parity bit is appended to the data
  Choosen according to the number of 1 bits in the message
    odd or even
An example using even parity
  Original message: 1011010
  A 0 bit is added to the end: 10110100
  m=8 and r=1 in this case
The distance of this code is 2, since any single-bit error produces a codeword with the wrong parity.

## Slide 36: Checksums
Idea:
  Add up the bytes in the data
  Include the sum in the frame
Use ones-complement arithmetic
Lower overhead than parity: 16 bits per frame
But, not resilient to errors
  Why?
Used in UDP, TCP, and IP
Data
START
END
Checksum
0101001
1101001= 10010010
+
0
1
Notes: Multiple values can sum to same checksum

## Slide 37: Cyclic Redundancy Check (CRC)
Uses field theory to compute a semi-unique value for a given message
Much better performance than previous approaches
  Fixed size overhead per frame (usually 32-bits)
  Quick to implement in hardware
  Only 1 in 232 chance of missing an error with 32-bit CRC

## Slide 38: CRC (Cyclic Redundancy Check)
Polynomial code
  Treating bit strings as representations of polynomials with coefficients of 0 and 1.
CRC
  Add k bits of redundant data to an n-bit message.
  Represent n-bit message as an n-1 degree polynomial;
    e.g., MSG=10011010 corresponds to M(x) = x7+ x4 + x3 + x1.
  Let k be the degree of some divisor polynomial G(x);
    e.g., G(x) = x3+ x2 + 1.
    Generator polynomial
      Agreed upon it in advance

## Slide 39: CRC
Transmit polynomial P(x) that is evenly divisible by G(x), and receive polynomial P(x) + E(x);
  E(x)=0 implies no errors.
Recipient divides (P(x) + E(x)) by G(x);
  the remainder will be zero in only two cases:
    E(x) was zero (i.e. there was no error),
    or E(x) is exactly divisible by C(x).
Choose G(x) to make second case extremely rare.

## Slide 40: A basic example with numbers
Make all legal messages divisible by 3
If you want to send 10
  First multiply by 4 to get 40
  Now add 2 to make it divisible by 3 = 42
When the data is received ..
  Divide by 3, if there is no remainder there is no error
  If no error, divide by 4 to get sent message
If we receive 43, 44, 41, 40, then error
45 would not be recognized as an error

## Slide 41: Mod 2 arithmetic
Operations are done modulo 2
1111
+1010
=====
0101
11001
x 101
=====
11001
+ 11001
=========
1111101

## Slide 42: A basic example with polynomials
Sender:
  multiply M(x) = x7+ x4 + x3 + x1 by xk; for our example, we get
    x10 + x7 + x6 + x4 (10011010000);
  divide result by C(x) (1101);
  Send 10011010000 + 101 = 10011010101,
  since this must be exactly divisible by C(x);
11111001
10011010000 Message
1101
1001
1101
1000
1101
1011
1101
1100
1101
1000
1101
101 Remainder
Generator 1101

## Slide 43: Further properties
Want to ensure that G(x) does not divide evenly into polynomial E(x).
All single-bit errors, as long as the xk and x0 terms have non-zero coefficients.
All double-bit errors, as long as G(x) has a factor with at least three terms.
Any odd number of errors, as long as G(x) contains the factor (x + 1).
Any “burst” error (i.e sequence of consecutive errored bits) for which the length of the burst is less than k bits.
Most burst errors of larger than k bits can also be detected.