## Slide 1: Computer Networks
Lecture 8: Interconnecting LANs
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2: Just Above the Data Link Layer
Bridging
  How do we connect LANs?
Function:
  Route packets between LANs
Key challenges:
  Plug-and-play, self configuration
  How to resolve loops
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Recap
Pros: Simplicity
  Hardware is stupid and cheap
Cons: No scalability
  More hosts = more collisions = pandemonium
Originally, Ethernet was a broadcast technology
Tee Connector
Terminator
Hub
Repeater

## Slide 4: Bridging the LANs
Bridging limits the size of collision domains
  Vastly improves scalability
  Question: could the whole Internet be one bridging domain?
Tradeoff: bridges are more complex than hubs
  Physical layer device vs. data link layer device
  Need memory buffers, packet processing hardware, routing tables
Hub
Hub

## Slide 5: Bridges
Original form of Ethernet switch
Connect multiple IEEE 802 LANs at layer 2
Goals
  Reduce the collision domain
  Complete transparency
    “Plug-and-play,” self-configuring
    No hardware of software changes on hosts/hubs
    Should not impact existing LAN operations
Hub
Forwarding of frames
Learning of (MAC) Addresses
Spanning Tree Algorithm (to handle loops)

## Slide 6: Frame Forwarding Tables
00:00:00:00:00:DD | 1 | 3 minutes
Each bridge maintains a forwarding table
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 1 minute
00:00:00:00:00:BB | 2 | 7 minutes
00:00:00:00:00:CC | 3 | 2 seconds

## Slide 7: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error Prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port
Hub
00:00:00:00:00:AA
00:00:00:00:00:BB
Port 1
Port 2
00:00:00:00:00:BB | 2 | 0 minutes
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 0 minutes
Delete old entries after a timeout

## Slide 8: The Danger of Loops
<Src=AA, Dest=DD>
This continues to infinity
  How do we stop this?
Remove loops from the topology
  Without physically unplugging cables
802.1 (LAN architecture) uses an algorithm to build and maintain a spanning tree for routing
AA
Port 1
Hub
Port 1
Hub
Port 2
Port 2
AA | 1
AA | 1
BB
CC
DD
AA | 2
AA | 2
AA | 1
AA | 1

## Slide 9: Spanning Tree Definition
A subset of edges in a graph that:
  Span all nodes
  Do not create any cycles
This structure is a tree
1
4
2
5
6
3
7
1
4
2
5
6
3
7
5
1
4
2
6
3
7

## Slide 10: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 11: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BPDUs:
Based on received BPDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to root)
Root ID
Path Cost to Root
Bridge ID

## Slide 12: Spanning Tree Construction
0: 0/0
12: 12/0
3: 3/0
27: 27/0
41: 41/0
9: 9/0
68: 68/0
27: 0/1
12: 0/1
41: 3/1
68: 9/1
41: 0/2
3: 0/2
68: 3/2
9: 3/2
68: 0/3
9: 0/3

## Slide 13: Bridges vs. Switches
Bridges make it possible to increase LAN capacity
  Reduces the amount of broadcast packets
  No loops
Switch is a special case of a bridge
  Each port is connected to a single host
    Either a client machine
    Or another switch
  Links are full duplex
  Simplified hardware: no need for CSMA/CD!
  Can have different speeds on each port

## Slide 14: Switching the Internet
Capabilities of switches:
  Network-wide routing based on MAC addresses
  Learn routes to new hosts automatically
  Resolve loops
Could the whole Internet be one switching domain?
NO
Notes: Flooding packets until routes figured out
No load balancing
Addressing!

## Slide 15: Limitations of MAC Routing
Inefficient
  Flooding packets to locate unknown hosts
Poor Performance
  Spanning tree does not balance load
  Hot spots
Extremely Poor Scalability
  Every switch needs every MAC address on the Internet in its routing table!
  IP addresses these problems (next …)

## Slide 16: Computer Networks
Lecture 8: Network Layer
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 17: Network Layer
Function:
  Route packets end-to-end on a network, through multiple hops
Key challenge:
  How to represent addresses
  How to route packets
    Scalability
    Convergence
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 18: Routers, Revisited
How to connect multiple LANs?
LANs may be incompatible
  Ethernet, Wifi, etc…
Connected networks form an internetwork
  The Internet is the best known example
Routers

## Slide 19: Internetworking Issues
Naming / Addressing
  How do you designate hosts?
Routing
  Must be scalable (i.e. a switched Internet won’t work)
Service Model
  What gets sent?
  How fast will it go?
  What happens if there are failures?
  Must deal with heterogeneity
    Remember, every network is different
Internet Service Model
Best-effort (i.e. things may break)
Store-and-forward datagram network
Lowest common denominator

## Slide 20: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 21: Possible Addressing Schemes
Flat
  e.g. each host is identified by a 48-bit MAC address
  Router needs an entry for every host in the world
    Too big
    Too hard to maintain (hosts come and go all the time)
    Too slow (more later)
Hierarchy
  Addresses broken down into segments
  Each segment has a different level of specificity
Notes: If time, show correlation between lookup speed and maximum line rate

## Slide 22: Example: Telephone Numbers
1-617-373-1234
West Village H
Room 256
Very General
Very Specific
West Village G
Room 1234
3278
Updates are Local

## Slide 23: Binary Hierarchy Example
1**
10*
11*
100
101
110
111
0**
00*
01*
000
001
010
011
Datagram, Destination = 101

## Slide 24: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g. 192.168.21.76
  Each number is a byte
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31

## Slide 25: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers

## Slide 26: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: NEU
129.10.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24

## Slide 27: How Do You Get IPs?
IP address ranges controlled by IANA
  Internet Assigned Number Authority
  Roots go back to 1972, ARPANET, UCLA
  Today, part of ICANN
IANA grants IPs to regional authorities
  ARIN (American Registry of Internet Numbers) may grant you a range of IPs
  You may then advertise routes to your new IP range
  There are now secondary markets, auctions, …

## Slide 28: Two Level Hierarchy
…
…
Host
Network
Subtree size determined by network class
Pfx

## Slide 29: Class Sizes
Class | Prefix Bits | Network Bits | Number of Classes | Hosts per Class
A | 1 | 7 | 27 – 2 = 126 (0 and 127 are reserved) | 224 – 2 = 16,777,214 (All 0 and all 1 are reserved)
B | 2 | 14 | 214 = 16,398 | 216 – 2 = 65,534 (All 0 and all 1 are reserved)
C | 3 | 21 | 221 = 2,097,512 | 28 – 2 = 254 (All 0 and all 1 are reserved)
 |  |  | Total: 2,114,036 | 
Too many network IDs
Too small to be useful
Way too big

## Slide 30: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:

## Slide 31: Subnet Example
Extract network:
Extract host:
10110101 11011101 01010100 01110010
IP Address:
& 11111111 11111111 11000000 00000000
Subnet Mask:
10110101 11011101 01000000 00000000
Result:
10110101 11011101 01010100 01110010
IP Address:
& ~(11111111 11111111 11000000 00000000)
Subnet Mask:
00000000 00000000 00010100 01110010
Result:

## Slide 32: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks

## Slide 33: Example Routing Table
Address Pattern | Subnet Mask | Destination Router
0.0.0.0 | 0.0.0.0 | Router 4
18.0.0.0 | 255.0.0.0 | Router 2
128.42.0.0 | 255.255.0.0 | Router 3
128.42.128.0 | 255.255.128.0 | Router 5
128.42.222.0 | 2555.255.255.0 | Router 1
Question: 128.42.222.198 matches four rows
  Which router do we forward to?
Longest prefix matching
  Use the row with the longest number of 1’s in the mask
  This is the most specific match

## Slide 34: Subnetting Revisited
Question: does subnetting solve all the problems of class-based routing?
NO
Classes are still too coarse
  Class A can be subnetted, but only 126 available
  Class C is too small
  Class B is nice, but there are only 16,398 available
Routing tables are still too big
  2.1 million entries per router

## Slide 35: Classless Inter Domain Routing
CIDR, pronounced ‘cider’
Key ideas:
  Get rid of IP classes
  Use bitmasks for all levels of routing
  Aggregation to minimize FIB (forwarding information base)
Arbitrary split between network and host
  Specified as a bitmask or prefix length
  Example: Stony Brook
    130.245.0.0 with netmask 255.255.0.0
    130.245.0.0 / 16

## Slide 36: Aggregation with CIDR
Original use: aggregating class C ranges
One organization given contiguous class C ranges
  Example: Microsoft, 207.46.192.* – 207.46.255.*
  Represents 26 = 64 class C ranges
  Specified as CIDR address 207.46.192.0/18
11001111
CF
207
00101110
2E
46
11xxxxxx
C0
192
xxxxxxxx
00
0
Decimal
Hex
Binary
0
8
16
24
31
18 Bits Frozen By Netmask
14 Arbitrary Bits

## Slide 37: Size of CIDR Routing Tables
From www.cidr-report.org
CIDR has kept IP routing table sizes in check
  Currently ~500,000 entries for a complete IP routing table
  Only required by backbone routers

## Slide 38: We had a special day in summer 2014!
512K day – August 12, 2014
Default threshold size for IPv4 route data in older Cisco routers  512K routes
  Some routers failed over to slower memory
    RAM vs. CAM (content addressable memory)
  Some routes dropped
Cisco issues update in May anticipating this issue
  Reallocated some IPv6 space for IPv4 routes
Part of the cause
  Growth in emerging markets
http://cacm.acm.org/news/178293-internet-routing-failures-bring-architecture-changes-back-to-the-table/fulltext

## Slide 39: Takeaways
Hierarchical addressing is critical for scalability
  Not all routers need all information
  Limited number of routers need to know about changes
Non-uniform hierarchy useful for heterogeneous networks
  Class-based addressing is too course
  CIDR improves scalability and granularity
Implementation challenges
  Longest prefix matching is more difficult than schemes with no ambiguity

## Slide 40: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 41: IP Datagrams
IP Datagrams are like a letter
  Totally self-contained
  Include all necessary addressing information
  No advanced setup of connections or circuits
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 42: IP Header Fields: Word 1
Version: 4 for IPv4
Header Length: Number of 32-bit words (usually 5)
Type of Service: Priority information (unused)
Datagram Length: Length of header + data in bytes
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
Limits packets to 65,535 bytes

## Slide 43: IP Header Fields: Word 3
Time to Live: decremented by each router
  Used to kill looping packets
Protocol: ID of encapsulated protocol
  6 = TCP, 17 = UDP
Checksum
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
Used to implement trace route

## Slide 44: IP Header Fields: Word 4 and 5
Source and destination address
  In theory, must be globally unique
  In practice, this is often violated
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 45: Problem: Fragmentation
Problem: each network has its own MTU
  DARPA principles: networks allowed to be heterogeneous
  Minimum MTU may not be known for a given path
IP Solution: fragmentation
  Split datagrams into pieces when MTU is reduced
  Reassemble original datagram at the receiver
MTU = 2000
MTU = 4000
MTU = 1500
Datagram
Dgram1
Dgram2
1
2
3
4

## Slide 46: IP Header Fields: Word 2
Identifier: a unique number for the original datagram
Flags: M flag, i.e. this is the last fragment
Offset: byte position of the first byte in the fragment
  Divided by 8
Version
HLen
TOS
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data

## Slide 47: Fragmentation Example
MTU = 2000
MTU = 4000
MTU = 1500
Data
Data
Data
IP Hdr
IP
IP
Length = 3820, M = 0
3800
20
Length = 2000, M = 1
Offset = 0
Length = 1840, M = 0
Offset = 1980
1980
20
1820
20
1980
+ 1820
= 3800

## Slide 48: Fragmentation Example
MTU = 2000
MTU = 1500
Data
Data
IP
IP
Data
Data
IP
IP
Length = 2000, M = 1
Offset = 0
Length = 1840, M = 0
Offset = 1980
1980
20
1820
20
20
20
1480
500
Length = 520, M = 1
Offset = 1480
Length = 1500, M = 1
Offset = 0
Data
Data
IP
IP
20
20
1480
340
Length = 360, M = 0
Offset = 3460
Length = 1500, M = 1
Offset = 1980
1480
+ 500
= 1980

## Slide 49: IP Fragment Reassembly
Performed at destination
M = 0 fragment gives us total data size
  360 – 20 + 3460 = 3800
Challenges:
  Out-of-order fragments
  Duplicate fragments
  Missing fragments
Basically, memory management nightmare
Data
IP
20
1480
Data
IP
20
500
Length = 520, M = 1, Offset = 1480
Length = 1500, M = 1, Offset = 0
Data
IP
20
1480
Data
IP
20
340
Length = 360, M = 0, Offset = 3460
Length = 1500, M = 1, Offset = 1980

## Slide 50: Fragmentation Concepts
Highlights many key Internet characteristics
  Decentralized and heterogeneous
    Each network may choose its own MTU
  Connectionless datagram protocol
    Each fragment contains full routing information
    Fragments can travel independently, on different paths
  Best effort network
    Routers/receiver may silently drop fragments
    No requirement to alert the sender
  Most work is done at the endpoints
    i.e. reassembly

## Slide 51: Fragmentation in Reality
Fragmentation is expensive
  Memory and CPU overhead for datagram reconstruction
  Want to avoid fragmentation if possible
MTU discovery protocol
  Send a packet with “don’t fragment” bit set
  Keep decreasing message length until one arrives
  May get “can’t fragment” error from a router, which will explicitly state the supported MTU
Router handling of fragments
  Fast, specialized hardware handles the common case
  Dedicated, general purpose CPU just for handling fragments

## Slide 52: Outline
Addressing
  Class-based
  CIDR
IPv4 Protocol Details
  Packed Header
  Fragmentation
IPv6

## Slide 53: The IPv4 Address Space Crisis
Problem: the IPv4 address space is too small
  232 = 4,294,967,296 possible addresses
  Less than one IP per person
Parts of the world have already run out of addresses
  IANA assigned the last /8 block of addresses in 2011
Region | Regional Internet Registry (RIR) | Exhaustion Date
Asia/Pacific | APNIC | April 19, 2011
Europe/Middle East | RIPE | September 14, 2012
North America | ARIN | 13 Jan 2015 (Projected)
South America | LACNIC | 13 Jan 2015 (Projected)
Africa | AFRINIC | 17 Jan 2022(Projected)

## Slide 54: IPv6
IPv6, first introduced in 1998(!)
  128-bit addresses
  4.8 * 1028 addresses per person
Address format
  8 groups of 16-bit values, separated by ‘:’
  Leading zeroes in each group may be omitted
  Groups of zeroes can be omitted using ‘::’
  2001:0db8:0000:0000:0000:ff00:0042:8329
  2001:0db8:0:0:0:ff00:42:8329
  2001:0db8::ff00:42:8329

## Slide 55: IPv6 Trivia
Who knows the IP for localhost?
  127.0.0.1
What is localhost in IPv6?
  ::1

## Slide 56: IPv6 Header
Double the size of IPv4 (320 bits vs. 160 bits)
Version
DSCP/ECN
Flow Label
0
8
16
24
31
4
12
19
Datagram Length
Next Header
Hop Limit
Source IP Address
Destination IP Address
Version = 6
Groups packets into flows, used for QoS
Same as IPv4
Same as Protocol in IPv4
Same as TTL in IPv4
Same as IPv4

## Slide 57: Differences from IPv4 Header
Several header fields are missing in IPv6
  Header length – rolled into Next Header field
  Checksum – was useless, so why keep it
  Identifier, Flags, Offset
    IPv6 routers do not support fragmentation
    Hosts are expected to use path MTU discovery
Reflects changing Internet priorities
  Today’s networks are more homogeneous
  Instead, routing cost and complexity dominate

## Slide 58: Performance Improvements
No checksums to verify
No need for routers to handle fragmentation
Simplified routing table design
  Address space is huge
  No need for CIDR (but need for aggregation)
  Standard subnet size is 264 addresses
Simplified auto-configuration
  Neighbor Discovery Protocol
  Used by hosts to determine network ID
  Host ID can be random!

## Slide 59: Additional IPv6 Features
Source Routing
  Host specifies the route to wants packet to take
Mobile IP
  Hosts can take their IP with them to other networks
  Use source routing to direct packets
Privacy Extensions
  Randomly generate host identifiers
  Make it difficult to associate one IP to a host
Jumbograms
  Support for 4Gb datagrams

## Slide 60: Deployment Challenges
Switching to IPv6 is a whole-Internet upgrade
  All routers, all hosts
  ICMPv6, DHCPv6, DNSv6
2013: 0.94% of Google traffic was IPv6, 2.5% today
IPv4
TCP, UDP, ICMP
HTTP, FTP, SMTP, RTP, IMAP, …
Ethernet, 802.11x, DOCSIS, …
Fiber, Coax, Twisted Pair, Radio, …

## Slide 61: Transitioning to IPv6
How do we ease the transition from IPv4 to IPv6?
  Today, most network edges are IPv6 ready
    Windows/OSX/iOS/Android all support IPv6
    Your wireless access point probably supports IPv6
  The Internet core is hard to upgrade
  … but a IPv4 core cannot route IPv6 traffic
Core
Internet
Business
Network
Home
Network
IPv6 Ready
IPv6 Ready
IPv4 Only :(
IPv6 Packets

## Slide 62: Transition Technologies
How do you route IPv6 packets over an IPv4 Internet?
Transition Technologies
  Use tunnels to encapsulate and route IPv6 packets over the IPv4 Internet
  Several different implementations
    6to4
    IPv6 Rapid Deployment (6rd)
    Teredo
    … etc.

## Slide 63: Network Layer, Control Plane
Function:
  Set up routes within a single network
Key challenges:
  Distributing and updating routes
  Convergence time
  Avoiding loops
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 64: Internet Routing
Internet organized as a two level hierarchy
First level – autonomous systems (AS’s)
  AS – region of network under a single administrative domain
  Examples: Comcast, AT&T, Verizon, Sprint, etc.
AS’s use intra-domain routing protocols internally
  Distance Vector, e.g., Routing Information Protocol (RIP)
  Link State, e.g., Open Shortest Path First (OSPF)
Connections between AS’s use inter-domain routing protocols
  Border Gateway Routing (BGP)
  De facto standard today, BGP-4

## Slide 65: AS Example
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 66: Why Do We Need ASs?
Routing algorithms are not efficient enough to execute on the entire Internet topology
Different organizations may use different routing policies
Allows organizations to hide their internal network structure
Allows organizations to choose how to route across each other (BGP)
Easier to compute routes
Greater flexibility
More autonomy/independence

## Slide 67: Routing on a Graph
Goal: determine a “good” path through the network from source to destination
What is a good path?
  Usually means the shortest path
  Load balanced
  Lowest $$$ cost
Network modeled as a graph
  Routers  nodes
  Link  edges
    Edge cost: delay, congestion level, etc.
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 68: Shortest Path Routing
Bellman-Ford Algorithm [Distance Vector]
Dijkstra’s Algorithm [Link State]
What does it mean to be the shortest (or optimal) route?
Minimize mean packet delay
Maximize the network throughput
Mininize the number of hops along the path

## Slide 69: Dijkstra’s Shortest Path Algorithm
Initially mark all nodes (except source) with infinite distance.
working node = source node
Sink node = destination node
While the working node is not equal to the sink
1. Mark the working node as permanent.
2. Examine all adjacent nodes in turn
If the sum of label on working node plus distance from working node to adjacent node is less than current labeled distance on the adjacent node, this implies a shorter path. Relabel the distance on the adjacent node and label it with the node from which the probe was made.
3. Examine all tentative nodes (not just adjacent nodes) and mark the node with the smallest labeled value as permanent. This node becomes the new working node.
Reconstruct the path backwards from sink to source.

## Slide 70: Dijkstra’s Algorithm
Dijkstra(graph (G,w), vertex s)
InitializeSingleSource(G, s)
S  
Q  V[G]
while Q  0 do
u  ExtractMin(Q)
S  S  {u}
for u  Adj[u] do
Relax(u,v,w)
InitializeSingleSource(graph G, vertex s)
for v  V[G] do
d[v]  
p[v]  0
d[s]  0
Relax(vertex u, vertex v, weight w)
if d[v] > d[u] + w(u,v) then
d[v]  d[u] + w(u,v)
p[v]  u
(V)
(1) ?
(E) times in total
executed (V) times

## Slide 71: Dijkstra’s Algorithm - Example
10
1
5
2
6
4
9
7
2
3

## Slide 72: Dijkstra’s Algorithm - Example
0




10
1
5
2
6
4
9
7
2
3

## Slide 73: Dijkstra’s Algorithm - Example
0
5
10


10
1
5
2
6
4
9
7
2
3

## Slide 74: Dijkstra’s Algorithm - Example
0
5
10


10
1
5
2
6
4
9
7
2
3

## Slide 75: Dijkstra’s Algorithm - Example
0
5
8
7
14
10
1
5
2
6
4
9
7
2
3

## Slide 76: Dijkstra’s Algorithm - Example
0
5
8
7
14
10
1
5
2
6
4
9
7
2
3

## Slide 77: Dijkstra’s Algorithm - Example
0
5
8
7
13
10
1
5
2
6
4
9
7
2
3

## Slide 78: Dijkstra’s Algorithm - Example
0
5
8
7
13
10
1
5
2
6
4
9
7
2
3

## Slide 79: Dijkstra’s Algorithm - Example
0
5
8
7
9
10
1
5
2
6
4
9
7
2
3

## Slide 80: Dijkstra’s Algorithm - Example
0
5
8
7
9
10
1
5
2
6
4
9
7
2
3

## Slide 81: Bellman-Ford Algorithm
BellmanFord(graph (G,w), vertex s)
InitializeSingleSource(G, s)
for i  1 to |V[G]  1| do
for (u,v)  E[G] do
Relax(u,v,w)
for (u,v)  E[G] do
if d[v] > d[u] + w(u,v) then
return false
return true

## Slide 82: Bellman-Ford Algorithm - Example
6
7
7
-3
2
8
-4
9
5
-2

## Slide 83: Bellman-Ford Algorithm - Example
0




6
7
7
-3
2
8
-4
9
5
-2

## Slide 84: Bellman-Ford Algorithm - Example
0
7
6


6
7
7
-3
2
8
-4
9
5
-2

## Slide 85: Bellman-Ford Algorithm - Example
0
7
6
2
4
6
7
7
-3
2
8
-4
9
5
-2

## Slide 86: Bellman-Ford Algorithm - Example
0
7
2
2
4
6
5
7
7
-3
2
8
-2
-4
9

## Slide 87: Bellman-Ford Algorithm - Example
0
7
2
-2
4
6
5
7
7
-3
2
8
-2
-4
9

## Slide 88: Bellman-Ford Algorithm - Complexity
BellmanFord(graph (G,w), vertex s)
InitializeSingleSource(G, s)
for i  1 to |V[G]  1| do
for (u,v)  E[G] do
Relax(u,v,w)
for (u,v)  E[G] do
if d[v] > d[u] + w(u,v) then
return false
return true
executed (V) times
(E)
(E)
(1)

## Slide 89: Internetwork Routing [Halsall]
Adaptive Routing
Centralized
Distributed
Intradomain routing
Interdomain routing
Distance Vector routing
Link State routing
[IGP]
[EGP]
[BGP,IDRP]
[OSPF,IS-IS,PNNI]
[RIP]
[RCC]
Interior
Gateway Protocols
Exterior
Gateway Protocols

## Slide 90: Routing Problems
Assume
  A network with N nodes
  Each node only knows
    Its immediate neighbors
    The cost to reach each neighbor
How does each node learn the shortest path to every other node?
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 91: Intra-domain Routing Protocols
Distance vector
  Routing Information Protocol (RIP), based on Bellman-Ford
  Routers periodically exchange reachability information with neighbors
Link state
  Open Shortest Path First (OSPF), based on Dijkstra
  Each network periodically floods immediate reachability information to all other routers
  Per router local computation to determine full routes

## Slide 92: Outline
Distance Vector Routing
  RIP
Link State Routing
  OSPF
  IS-IS

## Slide 93: Distance Vector Routing
What is a distance vector?
  Current best known cost to reach a destination
Idea: exchange vectors among neighbors to learn about lowest cost paths
Routing Information Protocol (RIP)
Destination | Cost
A | 7
B | 1
D | 2
E | 5
F | 1
DV Table
at Node C
No entry for C
Initially, only has info for immediate neighbors
  Other destinations cost = ∞
Eventually, vector is filled

## Slide 94: Distance Vector Routing Algorithm
Wait for change in local link cost or message from neighbor
Recompute distance table
If least cost path to any destination has changed, notify neighbors

## Slide 95: Distance Vector Initialization
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
Initialization:
for all neighbors V do
if V adjacent to A
D(A, V) = c(A,V);
else
D(A, V) = ∞;
…

## Slide 96: Distance Vector: 1st Iteration
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
8
C
D(A,D) = min(D(A,D), D(A,C)+D(C,D))
= min(∞, 7 + 1) = 8
3
B
5
B
D(A,C) = min(D(A,C), D(A,B)+D(B,C))
= min(7, 2 + 1) = 3
D(A,D) = min(D(A,D), D(A,B)+D(B,D))
= min(8, 2 + 3) = 5
2
C
4
B
3
B

## Slide 97: Distance Vector: End of 3rd Iteration
Dest. | Cost | Next
B | 2 | B
C | 3 | B
D | 4 | B
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 2 | C
Node B
Dest. | Cost | Next
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | 4 | C
B | 2 | C
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
Nothing changes, algorithm terminates
Until something changes…

## Slide 98
4
1
A
B
C
50
loop:
wait (link cost update or update message)
if (c(A,V) changes by d)
for all destinations Y through V do
D(A,Y) = D(A,Y) + d
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) = min(D(A, Y), D(A, V) + D(V, Y));
if (there is a new minimum for destination Y)
send D(A, Y) to all neighbors
forever
1
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
Link Cost Changes,
Algorithm Starts
Algorithm Terminates
Good news travels fast
Notes: Change circles to rectangles, don’t block the text

## Slide 99: Count to Infinity Problem
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | B
D | C | N
A | 7 | B
B | 1 | B
D | C | N
A | 8 | C
C | 1 | B
D | C | N
A | 7 | B
B | 1 | B
Node B knows D(C, A) = 5
However, B does not know the path is C  B  A
Thus, D(B,A) = 6 !
Bad news travels slowly

## Slide 100: Poisoned Reverse
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
D | C | N
A | 51 | C
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
If C routes through B to get to A
  C tells B that D(C, A) = ∞
  Thus, B won’t route to A via C