## Slide 1: Computer Networks
Lecture 9: Transport layer Part I
Based on slides from D. Choffnes Northeastern U. and P. Gill from StonyBrook University
Revised Autumn 2015 by S. Laki

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived connections
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 4: The Case for Multiplexing
Datagram network
  No circuits
  No connections
Clients run many applications at the same time
  Who to deliver packets to?
IP header “protocol” field
  8 bits = 256 concurrent streams
Insert Transport Layer to handle demultiplexing
Packet
Network
Data Link
Physical
Transport

## Slide 5: Demultiplexing Traffic
Endpoints identified by <src_ip, src_port, dest_ip, dest_port>
Network
Transport
Application
P1
P2
P3
P4
P6
P7
P5
Host 1
Host 2
Host 3
Unique port for each application
Applications share the same network
Server applications communicate with multiple clients

## Slide 6: Layering, Revisited
Application
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Lowest level end-to-end protocol
  Transport header only read by source and destination
  Routers view transport header as payload
Application
Transport
Network
Data Link
Physical
Network
Data Link
Layers communicate peer-to-peer

## Slide 7: User Datagram Protocol (UDP)
Simple, connectionless datagram
  C sockets: SOCK_DGRAM
Port numbers enable demultiplexing
  16 bits = 65535 possible ports
  Port 0 is invalid
Checksum for error detection
  Detects (some) corrupt packets
  Does not detect dropped, duplicated, or reordered packets
Destination Port
0
16
31
Payload Length
Source Port
Checksum

## Slide 8: Uses for UDP
Invented after TCP
  Why?
Not all applications can tolerate TCP
Custom protocols can be built on top of UDP
  Reliability? Strict ordering?
  Flow control? Congestion control?
Examples
  RTMP, real-time media streaming (e.g. voice, video)
  Facebook datacenter protocol

## Slide 9: Outline
UDP – already discussed
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 10: Transmission Control Protocol
Options
Reliable, in-order, bi-directional byte streams
  Port numbers for demultiplexing
  Virtual circuits (connections)
  Flow control
  Congestion control, approximate fairness
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
Why these features?
4
HLen

## Slide 11: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection

## Slide 12: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number
Client
Server
SYN <SeqC, 0>
SYN/ACK <SeqS, SeqC+1>
ACK <SeqC+1, SeqS+1>
Why
Sequence # +1?
Notes: Seq + 1  next expected data byte
211

## Slide 13: Connection Setup Issues
Connection confusion
  How to disambiguate connections from the same host?
  Random sequence numbers
Source spoofing
  Kevin Mitnick
  Need good random number generators!
Connection state management
  Each SYN allocates state on the server
  SYN flood = denial of service attack
  Solution: SYN cookies
Notes: Spoofing + sequence prediction to hijack connections
SYN cookie: special sequence number sent in SYNACK so that when ACK comes back SYN cookie value can be reconstructed

## Slide 14: Connection Tear Down
Either side can initiate tear down
Other side may continue sending data
  Half open connection
  shutdown()
Acknowledge the last FIN
  Sequence number + 1
What happens if 2nd FIN is lost?
Client
Server
FIN <SeqA, *>
ACK <*, SeqA+1>
ACK
Data
FIN <SeqB, *>
ACK <*, SeqB+1>

## Slide 15: Sequence Number Space
TCP uses a byte stream abstraction
  Each byte in each stream is numbered
  32-bit value, wraps around
  Initial, random values selected during setup. Why?
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550

## Slide 16: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
Data (1460 bytes)
Data/ACK (730 bytes)
Data/ACK (1460 bytes)
Seq.
Ack.
Seq.
Ack.
1
23
23
1461
1461
753
753
2921
Data and ACK in the same packet
23
1

## Slide 17: Flow Control
Problem: how many packets should a sender transmit?
  Too many packets may overwhelm the receiver
  Size of the receivers buffers may change over time
Solution: sliding window
  Receiver tells the sender how big their buffer is
  Called the advertised window
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Window may go to zero!

## Slide 18: Flow Control: Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
Must be buffered until ACKed
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 19: Sliding Window Example
1
2
3
4
5
6
7
5
6
7
Time
Time
TCP is ACK Clocked
Short RTT  quick ACK  window slides quickly
Long RTT  slow ACK  window slides slowly

## Slide 20: Observations
Throughput is ~ w/RTT
Sender has to buffer all unacknowledges packets, because they may require retransmission
Receiver may be able to accept out-of-order packets, but only up to buffer limits

## Slide 21: What Should the Receiver ACK?
ACK every packet
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension
Notes: Why is Cum. Ack a bad idea -> packets 0-10,000 ;; 0-999 are lost but 1000-10000 received. Cumack val = 0. Server will hold 9K bytes in buffer even though received successfully and may even retransmit them.

## Slide 22: Sequence Numbers, Revisited
32 bits, unsigned
  Why so big?
For the sliding window you need…
  |Sequence # Space| > 2 * |Sending Window Size|
  232 > 2 * 216
Guard against stray packets
  IP packets have a maximum segment lifetime (MSL) of 120 seconds
    i.e. a packet can linger in the network for 2 minutes
Notes: Paws = protection against wrapping sequence

## Slide 23: Silly Window Syndrome
Problem: what if the window size is very small?
  Multiple, small packets, headers dominate data
Equivalent problem: sender transmits packets one byte at a time
for (int x = 0; x < strlen(data); ++x)
write(socket, data + x, 1);
Header
Data
Header
Data
Header
Data
Header
Data

## Slide 24: Nagle’s Algorithm
If the window >= MSS and available data >= MSS:
  Send the data
Elif there is unACKed data:
  Enqueue data in a buffer until an ACK is received
Else: send the data
Problem: Nagle’s Algorithm delays transmissions
  What if you need to send a packet immediately?
  int flag = 1;
  setsockopt(sock, IPPROTO_TCP, TCP_NODELAY, (char *) &flag, sizeof(int));
Send a full packet
Send a non-full packet if nothing else is happening

## Slide 25: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
  Missing sequence numbers indicate lost packets
Lost segments detected by sender
  Use timeout to detect missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 26: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 27: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e. TCP is conservative)
Data
ACK
Sample

## Slide 28: RTT Sample Ambiguity
Karn’s algorithm: ignore samples for retransmitted segments
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Sample
Sample?

## Slide 29: Challenge of RTO in data centers
TCP Incast problem – E.g. Hadoop, Map Reduce, HDFS, GFS
Many senders sending simultaneously to receiver
Buffer at switch fills and packets are lost!
No ACKs will come back 
Wait RTO
Wait RTO
Wait RTO
Challenges:
Need to break synchronization
RTO estimation designed for wide area
Data centers have much smaller RTT
Notes: itt